## Slide 1: Hourly Power Data
European wholesale power — prices, generation & capacity
17 July 2026
ENTSO-E hourly data · auto-linked workbook

## Slide 2: Price volatility & negative-price hours
Annual volatility and the incidence of negative prices across the five markets
Source: ENTSO-E Transparency Platform (hourly prices, generation, flows & capacity).
Price volatility: annual SD of hourly day-ahead price (€/MWh)
Negative-price hours per year, by country
Chart: GB = Elexon market index (within-day), not a day-ahead auction
| 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
Germany | 15.52 | 17.5 | 73.68 | 142.82 | 47.58 | 52.73 | 52.09
Spain | 10.88 | 11.42 | 74.71 | 69.46 | 41.34 | 45.94 | 47.61
Portugal | 10.81 | 11.26 | 74.7 | 69.13 | 39.93 | 45.57 | 46.44
France | 14.02 | 16.11 | 84.31 | 145.84 | 45.53 | 40.66 | 46.38
Italy | 12.67 | 14.63 | 81.08 | 133.15 | 35.59 | 29.66 | 29.69
Great Britain
Chart: GB = Elexon market index (within-day), not a day-ahead auction
| 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
Germany | 211 | 298 | 139 | 70 | 300 | 457 | 576
Spain | 0 | 0 | 0 | 0 | 0 | 247 | 556
Portugal | 0 | 0 | 0 | 0 | 0 | 196 | 200
France | 27 | 102 | 64 | 4 | 147 | 352 | 513
Italy | 0 | 0 | 0 | 0 | 0 | 0 | 0
Great Britain

## Slide 3: Negative & extreme prices in detail (Germany)
How negative-hour incidence builds through the year, and the daily price range
Source: ENTSO-E Transparency Platform (hourly prices, generation, flows & capacity).
Cumulative near-negative-price hours through the year (Germany)
Daily minimum vs maximum price (Germany, 2025)
Chart: day of year
Chart: max EUR/MWh

## Slide 4: Intraday price shape & price duration
Average intraday price profile by year, and the full price distribution
Source: ENTSO-E Transparency Platform (hourly prices, generation, flows & capacity).
Intraday price shape by year, indexed to daily mean (Germany)
Price duration curves by year (Portugal)
Chart: hour of day (UTC)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23
2019 | 0.7721 | 0.7461 | 0.7387 | 0.7738 | 0.9055 | 1.0721 | 1.1763 | 1.1559 | 1.092 | 1.0408 | 0.9913 | 0.9352 | 0.9051 | 0.9249 | 0.9734 | 1.0838 | 1.2255 | 1.3174 | 1.2799 | 1.1608 | 1.0661 | 0.9764 | 0.874 | 0.813
2020 | 0.7574 | 0.7187 | 0.7029 | 0.7458 | 0.8905 | 1.0666 | 1.1929 | 1.1741 | 1.087 | 1.0181 | 0.9603 | 0.8779 | 0.8265 | 0.8626 | 0.9492 | 1.1067 | 1.3113 | 1.4441 | 1.3655 | 1.1902 | 1.0817 | 0.9834 | 0.879 | 0.8075
2021 | 0.7706 | 0.7456 | 0.7413 | 0.7799 | 0.913 | 1.0695 | 1.1878 | 1.1647 | 1.0992 | 1.0419 | 0.9974 | 0.9344 | 0.896 | 0.9237 | 0.9899 | 1.1178 | 1.2771 | 1.3402 | 1.2612 | 1.1297 | 1.0279 | 0.9357 | 0.8442 | 0.8111
2022 | 0.8372 | 0.8143 | 0.81 | 0.8564 | 0.9875 | 1.1114 | 1.1791 | 1.1165 | 1.0175 | 0.9349 | 0.8741 | 0.8171 | 0.794 | 0.8391 | 0.9193 | 1.0711 | 1.2462 | 1.3545 | 1.3122 | 1.1945 | 1.1062 | 1.0077 | 0.9271 | 0.8721
2023 | 0.8402 | 0.8162 | 0.8094 | 0.8489 | 0.9863 | 1.1422 | 1.182 | 1.1216 | 0.9948 | 0.894 | 0.8147 | 0.7407 | 0.7126 | 0.7757 | 0.8939 | 1.0617 | 1.2757 | 1.4525 | 1.3938 | 1.2454 | 1.1294 | 1.034 | 0.951 | 0.8831
2024 | 0.8513 | 0.8299 | 0.8244 | 0.8705 | 1.0208 | 1.1649 | 1.19 | 1.0695 | 0.9075 | 0.7729 | 0.6775 | 0.6043 | 0.5981 | 0.6839 | 0.8611 | 1.1057 | 1.4067 | 1.6145 | 1.5878 | 1.3191 | 1.1483 | 1.0355 | 0.9563 | 0.8994
2025 | 0.9172 | 0.8967 | 0.9008 | 0.9477 | 1.0628 | 1.1869 | 1.2039 | 1.0825 | 0.871 | 0.7065 | 0.5853 | 0.5145 | 0.5226 | 0.6303 | 0.8081 | 1.0732 | 1.3794 | 1.5787 | 1.5373 | 1.3475 | 1.1921 | 1.087 | 1.0087 | 0.9592
2026 | 1.0233 | 1.0035 | 1.0045 | 1.0322 | 1.1164 | 1.1666 | 1.1353 | 0.9809 | 0.7877 | 0.627 | 0.4893 | 0.3853 | 0.3872 | 0.5126 | 0.7128 | 0.9842 | 1.2833 | 1.5412 | 1.6484 | 1.5017 | 1.3231 | 1.1916 | 1.1087 | 1.0595
Chart: day of year

## Slide 5: Intraday generation mix & price (Portugal, 2025)
Hourly generation by technology, with the wholesale price overlaid
Source: ENTSO-E Transparency Platform (hourly prices, generation, flows & capacity).
Intraday generation mix and price (Portugal, 2025)
Chart: hour of day (UTC)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23
Gas | 800.5 | 801.6 | 804.6 | 807.9 | 817.2 | 829.7 | 845.8 | 859.2 | 853.1 | 844.6 | 846.2 | 849.2 | 848.5 | 864.2 | 865.3 | 892.2 | 950.8 | 1016 | 1032.5 | 1038.3 | 1013.4 | 961.4 | 887.8 | 822.4
Biomass | 321 | 320.7 | 320.3 | 319.7 | 319 | 319.1 | 319.2 | 318.9 | 318.3 | 317.2 | 316.8 | 316.9 | 317.7 | 317.8 | 318.1 | 318.1 | 318.4 | 319.1 | 320.2 | 321 | 321.3 | 321.5 | 321.2 | 321.1
Hydro run-of-river | 1000.7 | 917.6 | 891.5 | 910.9 | 1011.8 | 1105.6 | 1126.7 | 1070.8 | 965.8 | 835.5 | 749.1 | 676.3 | 623.8 | 602.2 | 614.1 | 669.5 | 839.4 | 1168.9 | 1488.9 | 1640.3 | 1576.2 | 1412.6 | 1215.3 | 1105.7
Hydro reservoir | 340.3 | 306.9 | 291.9 | 297.5 | 339.6 | 425.8 | 472.1 | 445.4 | 350.8 | 278.4 | 239 | 226.5 | 218.1 | 217.6 | 233.8 | 267.3 | 359.7 | 536.5 | 706.5 | 816.1 | 731.7 | 577 | 469.6 | 399.1
Hydro pumped (production) | 549.9 | 429.9 | 378.2 | 413.6 | 576.3 | 884.9 | 976.8 | 777.3 | 455.1 | 242 | 158 | 131 | 112.2 | 115.5 | 136.9 | 224.2 | 545.6 | 1204 | 1811.5 | 2072.5 | 1874.4 | 1430.4 | 1071.6 | 767.5
Onshore wind | 1642.1 | 1644.4 | 1652.6 | 1657.2 | 1665.2 | 1668.5 | 1659.6 | 1595.8 | 1494.5 | 1402.4 | 1334.5 | 1302 | 1305 | 1326.4 | 1367.4 | 1418.8 | 1470.2 | 1513.6 | 1539.7 | 1574.7 | 1612 | 1634.6 | 1643.3 | 1646.7
Solar | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 10.6 | 133.3 | 505 | 1047.6 | 1544.9 | 1883.1 | 2056.2 | 2089.6 | 2046.1 | 1891.3 | 1600.8 | 1129.6 | 585.6 | 180.5 | 19.9 | 0.2 | 0.1 | 0.1 | 0.1
Other | 25.7 | 25.7 | 25.4 | 25 | 24.8 | 24.9 | 25 | 24.9 | 25 | 25 | 25 | 25.1 | 25.2 | 25.2 | 25.3 | 25.3 | 25.3 | 25.4 | 25.5 | 25.4 | 25.4 | 25.6 | 25.5 | 25.7
Price | 70.5 | 67 | 64.9 | 65.2 | 69.9 | 79.4 | 82.3 | 71.2 | 53.5 | 41.1 | 35 | 32.1 | 30 | 30 | 33.2 | 43 | 60.3 | 83.7 | 105.4 | 115.1 | 104.1 | 91.2 | 84 | 76.2

## Slide 6: Capture price vs baseload by technology (Germany)
How each technology's realised (capture) price compares with time-weighted baseload
Source: ENTSO-E Transparency Platform (hourly prices, generation, flows & capacity).
Capture price vs baseload by technology (Germany)
Chart: % vs base
| Solar | Onshore wind | Offshore wind | Hydro pumped (production) | Hydro reservoir | Hydro run-of-river | Biomass | Gas | Lignite | Hard coal
2019 | -7.33 | -14.2 | -7.74 | 24.06 | 11.71 | -0.23 | 0.47 | 10.46 | 8.6 | 19.03
2020 | -19.56 | -19.34 | -8.62 | -0.24 | 18.58 | -0.51 | 0.27 | 16.74 | 17.39 | 29.81
2021 | -22.09 | -16.64 | -4.65 | 28.48 | 11.18 | -6.69 | 1.01 | 10.99 | 10.31 | 29.5
2022 | -5.59 | -28.51 | -17.4 | 27.07 | 20.16 | 0.45 | 0.08 | 9.13 | 6.6 | 15.27
2023 | -24.16 | -17.43 | -9.06 | 31.97 | 16.6 | -1.62 | 1.97 | 15.38 | 15.59 | 22.52
2024 | -41.12 | -17.78 | -9.05 | 44.68 | 28.44 | -0.48 | 2.51 | 20.94 | 16.3 | 20.64
2025 | -48.44 | -13.4 | -4.24 | 45.52 | 27.45 | 1.06 | 3.94 | 23.59 | 16.68 | 25.12

## Slide 7: Installed generation capacity by technology (Germany)
Installed capacity by technology
Source: ENTSO-E Transparency Platform (hourly prices, generation, flows & capacity).
Installed generation capacity by technology (Germany)
Chart: MW
| Solar | Onshore wind | Offshore wind | Hydro pumped (production) | Hydro reservoir | Hydro run-of-river | Biomass | Gas | Lignite | Hard coal | Nuclear
2019 | 45435 | 52945.6 | 6393 | 9422 | 1309 | 4007.9 | 7782.1 | 31745 | 21205 | 25293 | 9516
2020 | 48376.4 | 53338.2 | 7503.7 | 9421.5 | 1308.5 | 3994.7 | 8033.6 | 31793.1 | 21067 | 22458.4 | 8114
2021 | 53537.9 | 54666.2 | 7773.8 | 9421.5 | 1308.5 | 3838.8 | 8447.1 | 32038.2 | 20487 | 23499.4 | 8114
2022 | 58002.3 | 55456.3 | 7786.8 | 9379.2 | 1309 | 3684.5 | 8378.9 | 30648.7 | 18544.3 | 18829.5 | 4056
2023 | 63366 | 57741.6 | 8128.8 | 9379 | 1345 | 3737.2 | 8513.8 | 33135 | 17692 | 18559 | 4056
2024 | 77015.6 | 60048.6 | 8456 | 9449 | 1392 | 3752.8 | 8659.5 | 37584 | 18365 | 18411
2025 | 86951.6 | 63403.2 | 9215 | 9383.8 | 1459.8 | 3923 | 8851 | 38596.6 | 15178 | 15951

## Slide 8: Intraday price shape — country variants
Spain's solar 'duck' in the indexed profile, and Germany's absolute price belly
Source: ENTSO-E Transparency Platform (hourly prices, generation, flows & capacity).
Spain — intraday price shape, indexed to daily mean
Germany — intraday price shape (€/MWh)
Chart: hour of day (UTC)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23
2019 | 0.9061 | 0.8718 | 0.8545 | 0.8604 | 0.8944 | 0.9586 | 1.0297 | 1.0604 | 1.0666 | 1.0601 | 1.0513 | 1.0429 | 1.0159 | 0.9788 | 0.958 | 0.9694 | 1.0079 | 1.063 | 1.1092 | 1.1317 | 1.0931 | 1.0384 | 1.0153 | 0.9624
2020 | 0.8751 | 0.8319 | 0.8111 | 0.8215 | 0.8858 | 0.9629 | 1.0354 | 1.0647 | 1.0562 | 1.0421 | 1.0356 | 1.0237 | 0.9968 | 0.9489 | 0.9305 | 0.9609 | 1.0327 | 1.12 | 1.1858 | 1.2032 | 1.1571 | 1.0688 | 1.0094 | 0.94
2021 | 0.9254 | 0.8945 | 0.8673 | 0.8686 | 0.9268 | 0.9956 | 1.0603 | 1.0697 | 1.0427 | 1.0062 | 0.9774 | 0.9592 | 0.9367 | 0.8967 | 0.8911 | 0.9452 | 1.0329 | 1.1264 | 1.1846 | 1.189 | 1.1361 | 1.064 | 1.0209 | 0.9829
2022 | 0.9481 | 0.9131 | 0.896 | 0.9061 | 0.96 | 1.044 | 1.0961 | 1.0756 | 1.0114 | 0.9489 | 0.9186 | 0.9013 | 0.8689 | 0.8403 | 0.8328 | 0.8761 | 0.9737 | 1.1094 | 1.2385 | 1.2729 | 1.2047 | 1.1015 | 1.0566 | 1.0053
2023 | 0.9757 | 0.9438 | 0.9194 | 0.9303 | 1.0045 | 1.1035 | 1.1621 | 1.1047 | 0.9602 | 0.846 | 0.7939 | 0.7607 | 0.7224 | 0.6924 | 0.7056 | 0.7961 | 0.9571 | 1.174 | 1.3689 | 1.4044 | 1.3159 | 1.1978 | 1.121 | 1.0393
2024 | 1.0188 | 0.9847 | 0.9566 | 0.9597 | 1.0305 | 1.168 | 1.2049 | 1.0979 | 0.8981 | 0.7428 | 0.6619 | 0.6263 | 0.5992 | 0.5827 | 0.6051 | 0.7343 | 0.9409 | 1.2047 | 1.4283 | 1.5666 | 1.4297 | 1.2844 | 1.1828 | 1.0911
2025 | 1.0733 | 1.0182 | 0.9882 | 0.996 | 1.0744 | 1.2294 | 1.2756 | 1.0803 | 0.7847 | 0.5911 | 0.4989 | 0.4519 | 0.4236 | 0.4205 | 0.4749 | 0.6319 | 0.9031 | 1.2701 | 1.6149 | 1.7713 | 1.5968 | 1.3924 | 1.2811 | 1.1575
2026 | 1.2323 | 1.1798 | 1.1433 | 1.1614 | 1.255 | 1.342 | 1.2388 | 0.9055 | 0.574 | 0.3981 | 0.323 | 0.2843 | 0.2743 | 0.2802 | 0.3185 | 0.4052 | 0.6106 | 1.1209 | 1.7229 | 1.9971 | 1.8703 | 1.6004 | 1.4397 | 1.3274
Chart: hour of day (UTC)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23
2019 | 29.08 | 28.1 | 27.82 | 29.15 | 34.11 | 40.38 | 44.31 | 43.54 | 41.13 | 39.2 | 37.34 | 35.23 | 34.09 | 34.84 | 36.67 | 40.82 | 46.16 | 49.62 | 48.21 | 43.73 | 40.16 | 36.78 | 32.92 | 30.62
2020 | 23.08 | 21.9 | 21.42 | 22.73 | 27.14 | 32.5 | 36.35 | 35.78 | 33.12 | 31.02 | 29.26 | 26.75 | 25.19 | 26.28 | 28.92 | 33.72 | 39.96 | 44.01 | 41.61 | 36.27 | 32.96 | 29.96 | 26.79 | 24.6
2021 | 74.64 | 72.21 | 71.8 | 75.53 | 88.42 | 103.58 | 115.04 | 112.8 | 106.46 | 100.9 | 96.6 | 90.49 | 86.77 | 89.46 | 95.87 | 108.26 | 123.69 | 129.8 | 122.15 | 109.42 | 99.56 | 90.63 | 81.76 | 78.56
2022 | 197.11 | 191.73 | 190.72 | 201.63 | 232.5 | 261.66 | 277.6 | 262.88 | 239.56 | 220.11 | 205.8 | 192.37 | 186.94 | 197.55 | 216.43 | 252.18 | 293.42 | 318.91 | 308.94 | 281.23 | 260.44 | 237.25 | 218.28 | 205.34
2023 | 79.97 | 77.68 | 77.04 | 80.8 | 93.88 | 108.71 | 112.5 | 106.75 | 94.68 | 85.08 | 77.54 | 70.5 | 67.82 | 73.83 | 85.08 | 101.05 | 121.42 | 138.24 | 132.65 | 118.53 | 107.49 | 98.41 | 90.51 | 84.05
2024 | 66.84 | 65.16 | 64.72 | 68.35 | 80.14 | 91.46 | 93.43 | 83.97 | 71.25 | 60.68 | 53.19 | 47.45 | 46.96 | 53.7 | 67.61 | 86.81 | 110.44 | 126.76 | 124.66 | 103.56 | 90.16 | 81.3 | 75.08 | 70.62
2025 | 81.93 | 80.1 | 80.46 | 84.66 | 94.94 | 106.03 | 107.54 | 96.7 | 77.8 | 63.11 | 52.28 | 45.96 | 46.68 | 56.3 | 72.18 | 95.86 | 123.22 | 141.02 | 137.33 | 120.37 | 106.49 | 97.1 | 90.11 | 85.68
2026 | 101.42 | 99.46 | 99.56 | 102.3 | 110.64 | 115.62 | 112.52 | 97.21 | 78.06 | 62.14 | 48.5 | 38.19 | 38.38 | 50.81 | 70.64 | 97.54 | 127.19 | 152.74 | 163.37 | 148.83 | 131.13 | 118.09 | 109.88 | 105.01

## Slide 9: Capture prices & negative hours — country variants
Portugal's technology capture spreads, and the rise of negative-price hours in Spain
Source: ENTSO-E Transparency Platform (hourly prices, generation, flows & capacity).
Portugal — capture price vs baseload by technology
Spain — cumulative near-negative-price hours through the year
Chart: % vs base
| Solar | Onshore wind | Hydro run-of-river | Hydro reservoir | Hydro pumped (production) | Biomass | Gas
2019 | 1.86 | -5.91 | 1.09 | 0.92 | 3.89 | -1.15 | 4.56
2020 | -2.22 | -5 | 6.86 | 15.14 | 15.08 | 0.32 | 13.21
2021 | -4.04 | -1.64 | -23.11 | -6.24 | 8.18 | 0.11 | 14.65
2022 | -10.08 | -5.54 | 4.47 | -7.7 | 9.31 | 1.46 | 6.63
2023 | -17.28 | -13.08 | 6.25 | 2.03 | 13.55 | 0.5 | 23.35
2024 | -32.7 | -12.95 | -1.33 | -3.17 | 21.55 | -2.24 | 29.24
2025 | -46.6 | -8.34 | 15.66 | 25.67 | 42.32 | 0.61 | 9.66
Chart: day of year

## Slide 10: Solar's imprint on the intraday market
The share of solar in the peak hour, and how the price 'duck' deepens month by month
Source: ENTSO-E Transparency Platform (hourly prices, generation, flows & capacity).
Solar share of the peak hour, by market (quarterly average)
Germany — intraday price by month (the monthly 'duck')
Chart: solar share of peak hour (%)
Great Britain
Chart: hour of day (UTC)
| 0.0 | 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0 | 21.0 | 22.0 | 23.0
Jan | 85.59 | 82.18 | 80.36 | 81.73 | 87.63 | 102.13 | 127.19 | 151.04 | 136.53 | 122.9 | 113.51 | 107.55 | 106.49 | 110.83 | 126.53 | 141.56 | 162.17 | 154.3 | 138.4 | 121.49 | 109.97 | 105.44 | 93.76 | 94.44
Feb | 108.98 | 106.42 | 104.47 | 106.47 | 110.28 | 125.37 | 151.48 | 165.83 | 144.35 | 125.57 | 113.85 | 107.68 | 107.43 | 113.07 | 124.79 | 142.01 | 164.93 | 172.99 | 161.08 | 143.7 | 129.95 | 124.96 | 115.79 | 112.77
Mar | 90.12 | 88.17 | 87.03 | 89.15 | 98.04 | 118.95 | 127.16 | 109.53 | 85.65 | 60.76 | 43.27 | 36.49 | 31.69 | 41.59 | 68.58 | 97.27 | 130.86 | 164.98 | 156.22 | 132.12 | 114.94 | 106.91 | 98.08 | 95.07
Apr | 82.49 | 81.95 | 83.44 | 91.3 | 110.23 | 124.03 | 105.41 | 76.52 | 50.32 | 32.54 | 15.27 | 3.01 | 4.17 | 20.15 | 38.34 | 70.05 | 107.61 | 138.62 | 144.38 | 118.3 | 104.39 | 93.56 | 89.93 | 84.19
May | 81.33 | 80.45 | 82.67 | 88.65 | 101.3 | 101.6 | 83.81 | 53.47 | 24.37 | 10.25 | -3.64 | -12.15 | -10.12 | 2.83 | 20.27 | 48.48 | 89.62 | 117.37 | 145.18 | 128.36 | 110.03 | 95.93 | 91.23 | 84.48
Jun | 79.79 | 78.16 | 79.13 | 83.72 | 92.04 | 86.89 | 71.39 | 43.5 | 20.36 | 7.7 | -2.04 | -10.09 | -10.45 | -1.62 | 11.14 | 41.59 | 78.67 | 107.69 | 143.12 | 143.15 | 118.92 | 99.88 | 90.62 | 83.39
Jul | 91.22 | 89.35 | 90.16 | 94.7 | 104.92 | 105.41 | 100.08 | 83.98 | 68.65 | 58.29 | 46.74 | 37.76 | 34.96 | 43.45 | 59.61 | 81.27 | 97.09 | 117.32 | 137.6 | 137.74 | 121.88 | 107.74 | 101.87 | 95.21
Aug | 83.49 | 81.99 | 84.29 | 91.66 | 101.38 | 101.94 | 90.5 | 69.51 | 49.58 | 31.17 | 19.29 | 12.42 | 14.06 | 24.93 | 39.34 | 72.14 | 100.64 | 133.32 | 144.5 | 121.17 | 106.01 | 95.75 | 91.49 | 85.94
Sep | 69.63 | 69.13 | 72.35 | 81.09 | 101.7 | 125.51 | 110.38 | 84.41 | 59.87 | 41.91 | 30.57 | 25.52 | 29.07 | 39.96 | 57.64 | 91.49 | 142.1 | 196.43 | 145.46 | 107.36 | 93.74 | 81.02 | 76.12 | 72.22
Oct | 62.59 | 60.58 | 61 | 64.36 | 79.47 | 107.03 | 114.36 | 98.19 | 82.71 | 71.64 | 62.14 | 57.73 | 61.08 | 72.29 | 85.31 | 109.29 | 141.56 | 146.06 | 108.44 | 89.02 | 81.64 | 73.23 | 70.05 | 64.59
Nov | 76.86 | 74.27 | 73.01 | 74.51 | 79.34 | 91.13 | 115.07 | 120.69 | 109.26 | 100.13 | 97.2 | 96.28 | 99.72 | 107.94 | 123.76 | 138.86 | 148.24 | 134.87 | 121.34 | 106.32 | 97.46 | 93.76 | 84.06 | 82.19
Dec | 73.12 | 70.59 | 69.55 | 70.38 | 74.55 | 84.3 | 97 | 108.45 | 106.1 | 98.27 | 94.99 | 93.01 | 95.86 | 103.84 | 114.12 | 119.47 | 118.7 | 111.88 | 104.67 | 97.76 | 90.89 | 89.02 | 80.13 | 75.67

## Slide 11: European power prices & renewables penetration
Monthly baseload price by market, and the rising share of wind & solar in generation
Source: ENTSO-E Transparency Platform (hourly prices, generation, flows & capacity).
Monthly baseload power price by market (€/MWh). GB is the Elexon market index, not a day-ahead auction
Wind & solar share of generation, by market (12-month average)
Chart: GB = Elexon market index (within-day), not a day-ahead auction
Great Britain
Chart: wind + solar, % of generation
Great Britain

## Slide 12: Renewable capture erosion & the net-load 'duck' (Germany)
How solar's realised price is eroded vs baseload, and how solar hollows out midday net load
Source: ENTSO-E Transparency Platform (hourly prices, generation, flows & capacity).
Solar & wind capture price vs baseload (Germany)
Net-load 'duck': demand − wind − solar by hour, by year (Germany)
Chart: capture vs baseload, %
Chart: net load, GW (demand − wind − solar)
| 0.0 | 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0 | 21.0 | 22.0 | 23.0
2019 | 31.06 | 30.92 | 31.66 | 33.53 | 37.41 | 41.26 | 43.1 | 42.1 | 40.03 | 38.31 | 36.71 | 35.54 | 35.22 | 36.21 | 38.4 | 41.8 | 45.63 | 47.55 | 46.65 | 43.68 | 40.61 | 37.49 | 34.32 | 32.24
2020 | 29.22 | 29.04 | 29.72 | 31.49 | 34.95 | 38.43 | 40.07 | 38.89 | 36.63 | 34.97 | 33.53 | 32.21 | 31.81 | 32.78 | 35.06 | 38.78 | 43.05 | 45.25 | 44.36 | 41.36 | 38.4 | 35.39 | 32.36 | 30.32
2021 | 33.71 | 33.54 | 34.24 | 36.03 | 39.51 | 42.84 | 44.27 | 43.02 | 40.73 | 38.91 | 37.38 | 36.01 | 35.4 | 36.34 | 38.7 | 42.62 | 46.92 | 49.16 | 48.37 | 45.54 | 42.71 | 39.79 | 36.82 | 34.74
2022 | 29.82 | 29.76 | 30.51 | 32.27 | 35.62 | 38.62 | 39.48 | 37.47 | 34.44 | 31.96 | 30.06 | 28.87 | 28.71 | 30.1 | 32.99 | 37.41 | 42.17 | 44.65 | 43.87 | 40.98 | 38.08 | 35.24 | 32.54 | 30.73
2023 | 25.37 | 25.25 | 25.89 | 27.61 | 30.89 | 33.81 | 34.58 | 32.56 | 29.43 | 26.86 | 24.93 | 23.71 | 23.53 | 24.94 | 28 | 32.66 | 37.6 | 40.27 | 39.65 | 36.89 | 33.93 | 31.02 | 28.27 | 26.36
2024 | 26.77 | 26.55 | 27.1 | 28.69 | 31.79 | 34.43 | 34.85 | 32.37 | 28.73 | 25.64 | 23.44 | 22.16 | 22.11 | 23.84 | 27.45 | 32.77 | 38.29 | 41.27 | 40.82 | 38.26 | 35.43 | 32.54 | 29.82 | 27.86
2025 | 27.46 | 27.23 | 27.84 | 29.58 | 32.75 | 35.17 | 34.87 | 31.38 | 26.71 | 22.92 | 20.23 | 18.94 | 19.07 | 21.16 | 25.34 | 31.31 | 37.88 | 41.7 | 41.67 | 39.1 | 36.15 | 33.23 | 30.42 | 28.48
2026 | 27.84 | 27.87 | 28.6 | 30.33 | 33.17 | 34.15 | 31.7 | 25.98 | 19.76 | 14.96 | 11.8 | 10.54 | 10.53 | 12.86 | 17.89 | 25.38 | 34.34 | 40.24 | 41.26 | 38.98 | 35.99 | 33.09 | 30.46 | 28.77

## Slide 13: Spain intraday 'duck' — quarterly, 2019 vs 2025
Average intraday price by quarter (Spain day-ahead)
Source: ENTSO-E Transparency Platform (hourly prices, generation, flows & capacity).
2019 — by quarter
2025 — by quarter

## Slide 14: Spain July price 'spaghetti' — 2019 vs 2025
Every July day's intraday price shape; navy line = July average (Spain)
Source: ENTSO-E Transparency Platform (hourly prices, generation, flows & capacity).
2019 — July, daily
2025 — July, daily